# DSL Driver Core API

## Data Structures

- struct DDC_atm_lut_t

Host based look up table to xref Channel Id's, VPI/VCI, LC, CID, packet type.

- struct DDC_DslPriv

DDC per-device data structure.

## Functions

- int DDC_atm_init (DDC_DslPriv **privP, void *dev, unsigned int OamTxQ, unsigned int OamRxQ)

Device Initialization.

- int DDC_atm_close (DDC_DslPriv **priv)

Device Shutdown.

- int DDC_sar_activate_vc (DDC_atm_activate_vc_parm_t *pVcPrm)

Activate one SAR channel.

- int DDC_sar_deactivate_vc (DDC_DslPriv *priv, int chan)

De-Activate one SAR channel.

- unsigned DDC_dsl_set_modulation (DDC_DslPriv *priv, void *data, int flag)

Set modulation.

- int DDC_dsl_clear_eoc_setup (DDC_DslPriv *priv)

Initialization for Clear EOC handling.

- int DDC_dsl_clear_eoc_send (DDC_DslPriv *priv, unsigned char *data, unsigned len, int ackFlag)

Send Clear EOC data.

- int DDC_dsl_clear_eoc_receive (DDC_DslPriv *priv)

Receive Clear EOC data.

- int DDC_dsl_clear_eoc_close (DDC_DslPriv *priv)

Close Clear EOC channel.

- int DDC_sar_handle_interrupt (DDC_DslPriv *priv, int irq, int *more)

SAR HAL ISR.

- int DDC_dsl_handle_interrupt (DDC_DslPriv *priv)

DSL HAL ISR.

- int DDC_dsl_generic_read (DDC_DslPriv *priv, int num, int *offset, unsigned *data)

Generic function to read one word (32-bit) from DSP host interface.

- int DDC_dsl_generic_write (DDC_DslPriv *priv, int num, int *offset, unsigned data)

Generic function to read one word (32-bit) from DSP host interface.

- int DDC_atm_set_lut (DDC_DslPriv *priv, void *vcc, int vpi, int vci, int chan)

Initialize one TX DMA channel.

- int DDC_atm_lut_clear (DDC_DslPriv *priv, int chan)

Clear one TX DMA channel.

- int DDC_atm_lut_find (DDC_DslPriv *priv, short vpi, int vci)

Find a TX DMA channel that matches a vpi/vci pair.

- int DDC_atm_walk_lut (DDC_DslPriv *priv)

Find a TX DMA channel that is not used.

- void DDC_dsl_chng_modulation (DDC_DslPriv *priv, void *data)

Configure Modem.

- void DDC_dsl_led_on (DDC_DslPriv *priv)

Turn on DSL link LED.

- void DDC_dsl_led_off (DDC_DslPriv *priv)

Turn off DSL link LED.

- void DDC_dsl_led_init (DDC_DslPriv *priv)

Initialize DSL link LED for HOST control.

- int DDC_sar_tx_flush (DDC_DslPriv *priv, int chan, int queue, int skip)

Call SAR HAL to flush TX queue.

- int DDC_sar_oam_generation (DDC_DslPriv *priv, int chan, int type, int vpi, int vci, int timeout)

Generate OAM data.

- void DDC_sar_stat_reset (void)

Reset AAL5 statistics.

- int DDC_atm_read_can_support_adsl2 (void)

This function returns a boolean value to indicate whether the chip supports ADSL2 and ADSL2+.

- int DDC_sar_send_packet (DDC_DslPriv *priv, int chan, void *new_skb, void *data, unsigned len, int pri)

Call SAR HAL to send a packet.

## Detailed Description

Author:

Copyright (C) 2001-2006 Texas Instruments Incorporated.

## Field Documentation

## struct DDC_atm_lut_t

int DDC_atm_lut_t::inuse

is DMA channel available (1=y)

int DDC_atm_lut_t::chanid

DMA channel ID (0-0x1f) This corresponds to the Channel ID that is used in the connection config reg (TN7ATM_CONN_CONFIG)

int DDC_atm_lut_t::vpi

Virtual path identifier

int DDC_atm_lut_t::vci

Virtual channel identifier

void* DDC_atm_lut_t::vcc

DDA call-back device structure.

int DDC_atm_lut_t::bClosing

Flag to indicate that the channel is closing

int DDC_atm_lut_t::ready

Flag to indicate that the channel is ready

int DDC_atm_lut_t::sarRxBuf

Number of Rx Buffers per channel

int DDC_atm_lut_t::sarRxMax

Number of Rx Buffers to be serviced per interrupt

int DDC_atm_lut_t::sarTxBuf

Number of Tx Buffers per channel

int DDC_atm_lut_t::sarTxMax

Number of Tx Buffers to be serviced per interrupt

## Field Documentation

## struct DDC_DslPriv

int DDC_DslPriv::lConnected

Flag to indicate whether the DSL link is up or not.

int DDC_DslPriv::dslInSync

Flag to indicate whether the DSL link is up or not.

int DDC_DslPriv::dsl_int

Default DSL Interrupt vector value

void* DDC_DslPriv::SarIsr

Pointer to SAR Interrupt handler

int DDC_DslPriv::int_num

Default SAR Interrupt vector value

int DDC_DslPriv::sar_freq

SAR frequency

int DDC_DslPriv::sarRxBuf

Number of Rx Buffers per channel

int DDC_DslPriv::sarRxMax

Number of Rx Buffers to be serviced per interrupt

int DDC_DslPriv::sarTxBuf

Number of Tx Buffers per channel

int DDC_DslPriv::sarTxMax

Number of Tx Buffers to be serviced per interrupt

int DDC_DslPriv::bTurboDsl

Flag to enable the Turbo-DSL feature.

DDC_atm_lut_t DDC_DslPriv::lut[MAX_DMA_CHAN+1]

SAR Channel DMA look up table (LUT)

int DDC_DslPriv::nohost_flag

Flag to disable the reading of the Host-DSP memory.

int DDC_DslPriv::bMarginRetrainEnable

Flag to enable the retrain based on margin

unsigned int DDC_DslPriv::dslReg

TBD

unsigned int DDC_DslPriv::def_sar_inter_pace

Default Interrupt pacing value

void* DDC_DslPriv::dev

The OS Specific device pointer.

PITIDSLHW_T DDC_DslPriv::pIhw

DSL_HAL structure

void* DDC_DslPriv::hnd_LED_0

Handle for the LED

## Define Documentation

#define ATM_NO_DMA_CHAN MAX_DMA_CHAN + 1

no tx dma channels available

#define ATM_SAR_INT 15

SAR interrupt

#define ATM_SAR_INT_PACING_BLOCK_NUM 2

Interrupt pacing module number

#define ATM_SAR_INT_RX_INT 34

RX interrupt number

#define ATM_SAR_INT_TX_INT 17

TX interrupt number

#define DDC_DSL_FINISHED 1

Not finished

#define DDC_DSL_NOT_FINISHED 0

Finished

#define EOC_DMA_CHAN MAX_DMA_CHAN

reserve this chan for clear eoc

| #define NUM_ELEMS | ( | x |  | ) | (sizeof(x)/sizeof(x[0])) |
| --- | --- | --- | --- | --- | --- |

Number of elements in an array

## Enumeration Type Documentation

enum ti_dsl_int_t

Enumerator:

| TI_SAR_INT | SAR interrupt |
| --- | --- |
| TI_DSL_INT | DSL interrupt |

## Function Documentation

| int DDC_atm_close | ( | DDC_DslPriv ** | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure (to be freed). |
| --- | --- | --- |

Returns:

0: Success

| int DDC_atm_init | ( | DDC_DslPriv ** | privP, |
| --- | --- | --- | --- |
|  |  | void * | dev, |
|  |  | unsigned int | OamTxQ, |
|  |  | unsigned int | OamRxQ |  |
|  | ) |  |  |  |

Parameters:

|  | privP | Pointer to main private data structure (to be initialized). |
| --- | --- | --- |
|  | dev | Pointer to device data structure provided by OS. |
|  | OamTxQ | The Tx queue to use. This is only valid for UR8. |
|  | OamRxQ | The Rx queue to use. This is only valid for UR8. |

Returns:

0: Success other: Failure

| int DDC_atm_lut_clear | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | chan |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | chan | Channel number |
| int DDC_atm_lut_find | ( | DDC_DslPriv * | priv, |
|  |  | short | vpi, |
|  |  | int | vci |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | vpi | VPI |
|  | vci | VCI |

Returns:

DMA channel number

| int DDC_atm_read_can_support_adsl2 | ( | void |  | ) |  |
| --- | --- | --- | --- | --- | --- |

Returns:

0: Success 1: Failure

| int DDC_atm_set_lut | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | void * | vcc, |
|  |  | int | vpi, |
|  |  | int | vci, |
|  |  | int | chan |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | vcc | VCC |
|  | vpi | VPI |
|  | vci | VCI |
|  | chan | Channel number |

Returns:

0: Success -1: Failure

| int DDC_atm_walk_lut | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |

Returns:

DMA channel number

| void DDC_dsl_chng_modulation | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | void * | data |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to DSL driver private data |
| --- | --- | --- |
|  | data | Command |

Returns:

0: Success -1: Failure

| int DDC_dsl_clear_eoc_close | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |

Returns:

0: Success other: Failure

| int DDC_dsl_clear_eoc_receive | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |

Returns:

0: Success other: Failure

| int DDC_dsl_clear_eoc_send | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | unsigned char * | data, |
|  |  | unsigned | len, |
|  |  | int | ackFlag |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | data | TBD. |
|  | len | TBD. |
|  | ackFlag | TBD. |

Returns:

0: Success other: Failure

| int DDC_dsl_clear_eoc_setup | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |

Returns:

0: Success

| int DDC_dsl_generic_read | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | num, |
|  |  | int * | offset, |
|  |  | unsigned * | data |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | num | Number of offset layers. |
|  | offset | Pointer to an array of offsets. |
|  | data | Pointer to data read. |

Returns:

0: Success

| int DDC_dsl_generic_write | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | num, |
|  |  | int * | offset, |
|  |  | unsigned | data |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | num | Number of offset layers. |
|  | offset | Pointer to an array of offsets. |
|  | data | Data to be written. |

Returns:

0: Success

| int DDC_dsl_handle_interrupt | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |

Returns:

0: Success

| void DDC_dsl_led_init | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to DSL driver private data |
| --- | --- | --- |

Returns:

None

| void DDC_dsl_led_off | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to DSL driver private data |
| --- | --- | --- |

Returns:

None

| void DDC_dsl_led_on | ( | DDC_DslPriv * | priv | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | priv | Pointer to DSL driver private data |
| --- | --- | --- |

Returns:

None

| unsigned DDC_dsl_set_modulation | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | void * | data, |
|  |  | int | flag |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to DSL driver private data |
| --- | --- | --- |
|  | data |  |
|  | flag |  |

Returns:

0: Success -1: Failure

| int DDC_sar_activate_vc | ( | DDC_atm_activate_vc_parm_t * | pVcPrm | ) |  |
| --- | --- | --- | --- | --- | --- |

Parameters:

|  | pVcPrm | Pointer to channel data structure with parameters to be used. |
| --- | --- | --- |

Returns:

0: Success -1: Failure

| int DDC_sar_deactivate_vc | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | chan |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | chan | Channel number. |

Returns:

0: Success -1: Failure

| int DDC_sar_handle_interrupt | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | irq, |
|  |  | int * | more |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | irq | TBD. |
|  | more | TBD. |

Returns:

0: Success

| int DDC_sar_oam_generation | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | chan, |
|  |  | int | type, |
|  |  | int | vpi, |
|  |  | int | vci, |
|  |  | int | timeout |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | chan | Channel number. |
|  | type |  |
|  | vpi | VPI |
|  | vci | VCI |
|  | timeout |  |

Returns:

0: Success -1: Failure

| int DDC_sar_send_packet | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | chan, |
|  |  | void * | new_skb, |
|  |  | void * | data, |
|  |  | unsigned | len, |
|  |  | int | pri |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | chan | Channel number to send packet. |
|  | new_skb | pointer to a packet. |
|  | data | pointer to data buffer of the packet. |
|  | len | length of the packet. |
|  | pri | priority of the packet. |

Returns:

0: Success 1: Failure

| void DDC_sar_stat_reset | ( | void |  | ) |  |
| --- | --- | --- | --- | --- | --- |

Returns:

None.

| int DDC_sar_tx_flush | ( | DDC_DslPriv * | priv, |
| --- | --- | --- | --- |
|  |  | int | chan, |
|  |  | int | queue, |
|  |  | int | skip |  |
|  | ) |  |  |  |

Parameters:

|  | priv | Pointer to main private data structure. |
| --- | --- | --- |
|  | chan | Channel number. |
|  | queue | Queue number. |
|  | skip | ??? |

Returns:

0: Success -1: Failure