# DSL SAR API

## Functions

- int DDC_cpsarCreateInstance (unsigned int instId, DDA_Handle hDDA, DDC_Handle **hDDC, void *param)

DDC_cpsarCreateInstance.

- int DDC_cpsarSend (CpsarDDCObj *hDDC, DDC_NetPktObj *pkt, int channel, void *sendArgs)

DDC_cpsarSend.

- int cpsarTxPktProcess (CpsarDDCObj *hDDC, int txQueue, int pktsToProcess, void *pktArgs)

cpsarTxPktProcess

- int cpsarRxPktProcess (CpsarDDCObj *hDDC, int rxQueue, int pktsToProcess, void *pktArgs)

cpsarTxPktProcess

- int cpsarTxBDProc (CpsarDDCObj *hDDC, unsigned int txQueue, int pktsPending, Bool *isEOQ)

cpsarTxBDProc

- int cpsarRxBDProc (CpsarDDCObj *hDDC, unsigned int rxQueue, int pktsPending, Bool *isEOQ)

cpsarRxBDProc

- int DDC_cpsarInit (CpsarDDCObj *hDDC, unsigned int useLB)

DDC_cpsarInit Initializes the DDC SAR device hardware, and enables the CPPI DMA block if necessary.

- int DDC_cpsarChClose (CpsarDDCObj *hDDC, int channel, int direction, void *chCloseArgs)

DDC_cpsarChClose

  - If DDC instance is in "Opened" state, disable the channel in hardware

  - Un-initialize the channel (free memory previously allocated).

- int DDC_cpsarDeleteInstance (CpsarDDCObj *hDDC, void *param)

DDC_cpsarDeleteInstance

  - delete the "instance" created via CreateInstance, and frees the DDC SAR structure pointer.

- int DDC_cpsarChOpen (CpsarDDCObj *hDDC, CpsarChInfo *chInfo, unsigned int QNum)

DDC_cpsarChOpen

  - Verify channel info (range checking etc)

  - Allocate memory for the channel

  - Book-keep operations for the channel - ready to be enabled in hardware.

- void ddc_cpsarDDCStats (CpsarDDCObj *hDDC, unsigned char ch)

DDC_cpsarChOpen

  - Reports the following statics for the given channel: TX Int Count, TX Teardown pending, TX Int with no active pkts, TX Out of BD's, RX Int Count, RX Teardown pending, RX Int with no active pkts, RX Out of Buffers, RX CRC Errors, RX Length Errors, RX Abort Errors.

## Function Documentation

| int cpsarRxBDProc | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | unsigned int | rxQueue, |
|  |  | int | pktsPending, |
|  |  | Bool * | isEOQ |  |
|  | ) |  |  |  |

- CPSAR DDC RX Buffer Descriptor processing

- processes received packets and passes them to DDA layer

- re-queues the buffer descriptor to the receive pool

- channel and queue validations should not be performed for speed

Note:

return number of pkts processed and returns TRUE in isEOQ and FALSE if pkt processing not completed.

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | rxQueue | Rx queue number |
|  | pktsPending | Number of packets to be processed. |
|  | isEOQ | Set to TRUE if End of Queue. |

Returns:

Number of packets processed

| int cpsarRxPktProcess | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | int | rxQueue, |
|  |  | int | pktsToProcess, |
|  |  | void * | pktArgs |  |
|  | ) |  |  |  |

- Handles the RX Processing in the Interrupt mode.

- Invokes cpsarRxBDProc, checks to see if EOQ was reached

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | rxQueue | Rx queue number |
|  | pktsToProcess | Not currently used. |
|  | pktArgs | Not currently used. |

Returns:

Number of packets processed

| int cpsarTxBDProc | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | unsigned int | txQueue, |
|  |  | int | pktsPending, |
|  |  | Bool * | isEOQ |  |
|  | ) |  |  |  |

- CPSAR DDC TX Buffer Descriptor processing

- processes transmit completed packets and returns the handles to DDA layer

- txqueue (0-4) indicates the completion queue to process

- channel and queue validations should not be performed for speed

Note:

returns number of pkts processed and returns false in isEOQ if pkt completion processing pending.

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | txQueue | Tx queue number |
|  | pktsPending | Number of packets to be processed. |
|  | isEOQ | Returns TRUE if End of Queue. |

Returns:

Number of packets processed

| int cpsarTxPktProcess | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | int | txQueue, |
|  |  | int | pktsToProcess, |
|  |  | void * | pktArgs |  |
|  | ) |  |  |  |

- Handles the TX Processing in the Interrupt mode.

- Invokes cpsarTxBDProc, checks return to see if EOQ was reached

- if EOQ not reached, don't EOI, retrigger the interrupt manually

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | txQueue | Tx queue number |
|  | pktsToProcess | packets to process in the current interrupt. |
|  | pktArgs | Not currently used. |

Returns:

Number of packets processed

| int DDC_cpsarChClose | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | int | channel, |
|  |  | int | direction, |
|  |  | void * | chCloseArgs |  |
|  | ) |  |  |  |

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | channel | The DMA channel to close. |
|  | direction | The direction to close the channel for. |
|  | chCloseArgs | This parameter is not used in this current implementation. |
| int DDC_cpsarChOpen | ( | CpsarDDCObj * | hDDC, |
|  |  | CpsarChInfo * | chInfo, |
|  |  | unsigned int | QNum |  |
|  | ) |  |  |  |

Parameters:

|  | hDDC | DDC SAR device Handle 0-15 = Recieve Queue Index for the RX channel. 16-31 = TX completion Queue Index for the TX channel. |
| --- | --- | --- |
|  | chInfo | The SAR channel information about the current channel. |

Note:

The channel number should be provided in the chInfo->channel field.

| int DDC_cpsarCreateInstance | ( | unsigned int | instId, |
| --- | --- | --- | --- |
|  |  | DDA_Handle | hDDA, |
|  |  | DDC_Handle ** | hDDC, |
|  |  | void * | param |  |
|  | ) |  |  |  |

CPSAR Instance creation function. DDA/DDC Handle and interface pointer exchange happens here.

Parameters:

|  | instId | Instance identifier |
| --- | --- | --- |
|  | hDDA | Handle to the DDA device structure |
|  | hDDC | Placeholder for Handle to the SAR device structure |
|  | param | Not used in this implementation. For future use. |

Returns:

Success or failure (PAL success/error code)

| void ddc_cpsarDDCStats | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | unsigned char | ch |  |
|  | ) |  |  |  |

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | ch | The SAR DMA channel to get the stats for. |
| int DDC_cpsarDeleteInstance | ( | CpsarDDCObj * | hDDC, |
|  |  | void * | param |  |
|  | ) |  |  |  |

Note:

"param" is not used in this implementation

| int DDC_cpsarInit | ( | CpsarDDCObj * | hDDC, |
| --- | --- | --- | --- |
|  |  | unsigned int | useLB |  |
|  | ) |  |  |  |

Parameters:

|  | hDDC | DDC SAR device Handle |
| --- | --- | --- |
|  | useLB | This tells the SAR to operate in Loopback mode or not. |
| int DDC_cpsarSend | ( | CpsarDDCObj * | hDDC, |
|  |  | DDC_NetPktObj * | pkt, |
|  |  | int | channel, |
|  |  | void * | sendArgs |  |
|  | ) |  |  |  |

- queues a packet onto a hardware queue

- supports multifragment packets

- no channel validation performed in the interest of speed

- sendArgs Bit Mapping as follows:

(Note: Bits 15-0 map directly to CPPI4 BD Word 2 bits 31-16.) 17-16 Priority Queue. 0-3. (Only valid for Ch 0) (currently we use only 0) 15-12 Packet Type 11 Descriptor Type (0 = Host, 1 = Embedded Mode) 10-8 Additional Buffer Count (0-7). Set to 0 for Host Mode. 7 Reserved 6-4 Protocol Specific Region Offset. Set to 0 for Host Mode. 3-0 Reserved.

Parameters:

|  | hDDC | Placeholder for Handle to the DDC layer |
| --- | --- | --- |
|  | pkt | Holds attributes of a network packet (NetBufObjs and packet size). |
|  | channel | Channel number. |
|  | sendArgs | See above. |

Returns:

Success or failure (PAL success/error code)