DSL Device Driver

User Guide

Important Notice: The products and services of Texas Instruments and its subsidiaries described herein are sold subject to our standard terms and conditions of sale. Customers are advised to obtain the most current and complete information about TI products and services before placing orders. TI assumes no liability for applications assistance, customer's applications or product designs, software performance, or infringement of patents. The publication of information regarding any other company's products or services does not constitute our approval, warranty or endorsement thereof.

Copyright © 2002 Texas Instruments Incorporated

Revision: 0.1

Revision Date: October 11, 2006

Texas Instruments Inc.

# Foreword

This document provides the description for building and interfacing with TI’s DSL device driver on Linux OS reference platform.

# Revision History

| Rev. | Date | Description | Author |
| --- | --- | --- | --- |
| 0.1 | 10/11/2006 | Created. |  |

# Contents

Foreword	2

Revision History	2

Contents	3

1	Introduction	4

2	References	5

3	Driver Architecture	6

4	Driver Directory Structure	7

4.1	Development Directory Structure	7

4.1.1	apps	7

4.1.2	build_op	7

4.1.3	dsl_drv	7

4.1.4	filesystems	7

4.1.5	libs	7

4.1.6	release	7

4.2	Release Directory Structure	7

4.2.1	dsl_drv	7

4.2.1.1	docs	7

4.2.1.1	src	7

4.2.1.1.1	dda	7

4.2.1.1.2	ddc	8

5	User Command Interface	9

6	Proc File	10

7	Environment Variable	11

8	Driver Functionality Description	12

8.1	Driver initialization	12

8.2	Packet transmission	12

8.3	Packet Reception	12

9	Build Environment	13

# Introduction

This document describes the DSL device driver. The details of CPSAR HAL and DSL HAL are excluded from this documentation. For references on them, please refer to [1] and [2].

# References

[1]	DSL HAL API Programmer's Guide

[2]	Communication Processor Hardware Abstraction Layer (CPHAL) API Reference Manual,

[3]	RGDK 1.0 Release Notes, 2006.

# Driver Architecture

On Linux, DSL driver is built as dynamically loadable modules. Figure 1 below shows the functional interfaces and software delineation of DSL driver.

# Driver Directory Structure

## Development Directory Structure

## apps

This directory contains application files.

The applications include BR2684CTL and UDEV.

## build_op

This directory contains output files generated by the build.

## dsl_drv

This directory is described below in “Release Directory Structure”.

## filesystems

This directory contains Linux file-system files.

## libs

This directory contains Linux library files used with DSL driver.

The libraries include LIBATM  and UCLIBC.

## release

This directory is described below in “Release Directory Structure”.

## Release Directory Structure

### dsl_drv

#### docs

This directory contains driver documents.

This file should reside in this directory.

#### src

This directory contains driver DDA/DDC source code.

##### dda

This directory contains OS-dependent DSL Driver Adaptation (DDA) Layer source code files.

This includes DDA for Linux 2.6.

The list of DDA files is given in the following table.

Table 1. DSL DDA Files

| Files | Description |
| --- | --- |
| dda_common.c | Contains miscellaneous OS-dependent functions provided. |
| dda_init_close.c | Contains OS-dependent initialization and closure processing functions. |
| dda_input.c | Contains OS-dependent environment variables processing functions. |
| dda_input.h | Header file for environment variables processing |
| dda_ti_dsl.h | Primary OS-dependent header file. |
| dda_txrx.c | Contains OS-dependent packet transmission/reception processing functions. |

##### ddc

This directory contains OS-independent DSL Driver Core (DDC) source code files.

The list of DDA files is given in the following table.

Table 2. DSL DDC Files

| Files | Description |
| --- | --- |
| ddc_clear_eoc.c | Contains Clear EOC processing functions. |
| ddc_common.c | Contains miscellaneous functions including statistics reporting. |
| ddc_init_close.c | Contains initialization and closure processing functions. |
| ddc_dsl_api.h | Header file for DSL DDC API functions. |
| ddc_ti_dsl.h | Primary header file. |
| ddc_txrx.c | Contains packet transmission/reception processing functions. |
| dev_host_interface.h | Header file for DSLSS DSP Host Interface. |
| dsl_hal_api.c | DSL HAL API functions. |
| dsl_hal_api.h | Header file for DSL HAL API functions. |
| dsl_hal_support.c | DSL HAL support functions. |
| dsl_hal_support.h | Header file for DSL HAL support functions. |
| dsl_hal_csl.c | DSL HAL chip support library functions. |
| dsl_hal_csl.h | Header file for DSL HAL chip support library functions. |
| ur08dsld_aa.bin | DSLSS DSP executable file for ADSL Annex A. |
| ur08dsld_ab.bin | DSLSS DSP executable file for ADSL Annex B. |
| ddc_sar_init.c | SAR HAL initialization and closure processing functions. |
| ddc_sar_txrx.c | SAR HAL packet transmission and reception processing functions. |

# User Command Interface

On Linux, DSL driver provides a single command interface that user application can call to pass command or information to the driver. To access this interface, user application needs to write a string to the proc file /proc/sys/dev/dslmod with the following,

echo command > /proc/sys/dev/dslmod

The list of commands supported is given in the following table. The commands are in string format. For example,

echo T1413 > /proc/sys/dev/dslmod

Table 3. User Command Description

(TO BE REVISITED)

| Command | Description |
| --- | --- |
| T1413 | Set DSL training mode to T1.413. |
| GDMT | Set DSL training mode to G.dmt. |
| GLITE | Set DSL training mode to G.Lite. |
| MMOD | Set DSL training mode to multi mode. |
| NMOD | Set no training mode. |
| AD2MOD | Set DSL training mode to ADSL2 |
| AD2DEL | Set DSL training mode to ADSL2 DELT |
| A2PMOD | Set DSL training mode to ADSL2+ mode |
| A2PDEL | Set DSL training mode to ADSL2+ DELT mode |
| tmode nn | Set DSL training mode based on bit cmd, where nn is the two-digit hex number, which specifies the training mode. |
| Exxxpyyyyc | Send end to end F5 cells with VPI=xxx and VCI=yyyy. xxx and yyyy are in decimal. |
| Sxxxpyyyyc | Send seg to seg F5 cells with VPI=xxx and VCI=yyyy. xxx and yyyy are in decimal. |
| exxxp0c | Send end to end F4 cells with VPI=xxx. |
| sxxxp0c | Send segment F4 cells with VPI=xxx. |
| exxxpyyyycdzzzt | Send end to end F5 cells with VPI=xxx and VCI=yyyy. xxx and yyyy are in decimal. zzz is time out value in millisecond |
| sxxxpyyyycdzzzt | Send seg to seg F5 cells with VPI=xxx and VCI=yyyy. xxx and yyyy are in decimal. zzz is time out value in millisecond. |
| Trellison | Set trellis on |
| Trellisoff | Set trellis off |
| Bitswapon | Set bitswap ON |
| Bitswapoff | Set bitswap OFF |

# Proc File Entry

On Linux, DSL driver provides several proc files for user application to retrieve information from the driver. The list of Proc entries supported is given in the following table.

Table 4. Proc File Description

(TO BE REVISITED)

| File name and path | Description |
| --- | --- |
| /proc/avalanche/avsar_modem_stat | Statistics for SAR and DSL. |
| /proc/avalanche/avsar_modem_training | First line: modem training state. |
| /proc/avalanche/avsar_ver | Version information for the Driver, PDSP, DSP, and etc. |
| /proc/avalanche/avsar_oam_ping | Oam ping result. |
| /proc/avalanche/avsar_pvc_table | Received PVC table information. |
| /proc/avalanche/avsar_sarhal_stats | Unformatted SAR HAL statistics. (debug only) |
| /proc/avalanche/avsar_channels | Channel information. (debug only) |

# Environment Variable

The environment variables used by DSL driver are given in the following table. Those variables that should not be modified by user applications are excluded from the list (Italic).

Table 5. Environment Variable Description

| Name | Type | Description |
| --- | --- | --- |
| ATM_ETSI | String | ETSI address string. |
| autopvc_enable | Integer | 0: off; 1: on. |
| Bitswap | Integer | 0: off; 1: on. |
| cpufrequency | Integer | Host CPU frequency. |
| dgas_polarity | Integer | DSLSS DSP setting. |
| DSL_BIT_TMODE | Integer | 0: off; 1: on. |
| DSL_FEATURE_CNTL_0 | Integer | DSLSS DSP IOP setting. |
| DSL_FEATURE_CNTL_1 | Integer | DSLSS DSP IOP setting. |
| DSL_PHY_CNTL_0 | Integer | DSLSS DSP PHY control setting. |
| DSL_PHY_CNTL_1 | Integer | DSLSS DSP PHY control setting. |
| DSL_UPG_DONE | Integer | Unused. |
| dsp_freq (AR7 only) | Integer | DSP Frequency: 250: 250 Mhz; other value: 200 Mhz. |
| dsp_noboost (AR7 only) | Integer | 0: off; 1: on. |
| enable_margin_retrain | Integer | 0: off; 1: on. |
| enable_rate_adapt | Integer | 0: off; 1: on. |
| eoc_vendor_id | Hex | Eight (8) ASCII bytes. |
| eoc_vendor_revision | Integer | 4-byte ADSL1 EOC vendor revision. |
| eoc_vendor_serialnum | String | 32-byte EOC vendor serial number. |
| fine_gain_control | Integer | DSLSS DSP setting. |
| fine_gain_value | Hex | DSLSS DSP setting. |
| invntry_vernum | Integer | 16-byte ADSL2/2+ EOC vendor revision. |
| los_alarm | Integer | 0: off; 1: on. |
| margin_threshold | Integer | Margin threshold. |
| maximum_bits_per_carrier | Integer | DSLSS DSP setting. |
| maximum_interleave_depth | Integer | DSLSS DSP setting. |
| modulation | Integer | Modem training mode same as defined in User Command. |
| oam_lb_timeout | Integer | OAM loopback timeout in milliseconds. |
| pair_selection | Integer | DSLSS DSP setting. |
| sar_ipacemax | Integer | SAR interrupt pacing value |
| SarLB | Integer | 0: off; 1: on. |
| SarRxBuf | Integer | Number of Rx buffers per channel. |
| SarRxMax | Integer | Number of Rx buffers to be serviced per interrupt. |
| SarTxBuf | Integer | Number of Tx buffers per channel. |
| SarTxMax | Integer | Number of Tx buffers to be serviced per interrupt. |
| trellis | Integer | 0: off; 1: on. |
| TurboDSL | Integer | 0: off; 1: on. |

# Driver Functionality Description

## Driver initialization

DSL driver is initialized through the DDA_atm_detect function. The DDA_atm_detect  function allocates memory for the private data structure used by DSL driver and calls the initialization routines of SAR HAL and DSL HAL to initialize both SAR and DSL subsystems . Upon completion of DDA_atm_detect  function the driver is ready to accept socket calls from ATM applications at user level. Interrupt registrations are also handled in DDA_atm_init . The DDA_atm_open function is called when a user applications such as PPPoE or BR2684ctl makes a socket call to the driver to open a new connection to the SAR interface.

The DDA_atm_open  function initializes the VCC structure with the appropriate ATM VPI/VCI and QoS options. The ATM device operation structure is shown below.

static const struct atmdev_ops DDA_atm_ops = {

open:           DDA_atm_open,

close:          DDA_atm_close,

ioctl:          DDA_atm_ioctl,

send:           DDA_atm_send,

change_qos:     DDA_atm_change_qos,

};

## Packet transmission

Once a proper VPI/VCI pair is initialized through user application, data can be transmitted through the DDA_atm_send function. The DDA_atm_send function checks the status of DSL interface and DSL modem to ensure that a valid connection is available to send data on. The type of data is also checked and a determination is made to whether to queue the packet to high priority queue or low priority queue for further data transmission. The driver checks whether there is packets to send in every DDA_atm_send call. If there is any packet to be sent, the driver will locate channel information from vcc structure and call SAR HAL send routine to send out packet. The packets are de-queued from priority queue first.  Upon completion, the SAR interrupt is handled through the DDA_atm_sar_irq function. The DDA_atm_sar_irq calls the interrupt handle routine of SAR HAL which in turn calls the DDA_atm_send_complete to free the packets.

## Packet Reception

The ATM driver processes the reception of incoming packets (i.e., from DSL interface) through the registered SAR interrupt (DDA_atm_sar_irq). DDA_atm_sar_irq calls SAR HAL interrupt handling routine which in turn calls the DDA_atm_receive to pass on received packets. If no errors exist within the PDU,  skb is passed to the IP stack through the atm_charge and vcc->push routines.  The SAR HAL will call DDA_atm_allocate_rx_skb  to replenish the used skb.

# Build Environment

Refer to [3] for detailed description of how to build a RGDK image with DSL device driver included.

# Text boxes

OS (br2684ctl)

proc files

Packets to OS

CLI or proc file/ioctl

Driver (un)load

Packets from OS

RX Routines

TX Routines

Init / Close

VC open/close

OS:  Linux operating system.

CLI: Command line interface or any user space applications.

Proc file: Application and kernel (driver) interface for Linux.

IOCTL: I/O interface between application and the driver.

Figure 1. DSL driver architecture and module interactions.

Linux DSL Driver

Software covered by this documents.

Hardware

ISR

Datapump

OS Wrapper/Interface

DSL HAL

OS Wrapper/Interface

SAR  HAL & Firmware